## Slide 1: ACME Talks

## Slide 2: Agenda
History, Bluetooth vs Bluetooth Smart (Bluetooth Low Energy)
Bluetooth Smart Ready
Protocol Basics

## Slide 3: History
Introduced by Nokia in 2006
  named Wibree / Baby Bluetooth
Merged into the main Bluetooth standard in 2010
  Bluetooth Core Specification Version 4.0
The Bluetooth SIG predicts: by 2018 more than 90 percent of Bluetooth-enabled smartphones will support Bluetooth Smart
The first cell phone to feature Bluetooth 4.0: iPhone 4S

## Slide 4: Bluetooth vs Bluetooth Smart

## Slide 5: Bluetooth Smart Ready
Single-mode: BLE, Bluetooth Smart devices
  ex. a heart rate sensor
Dual-mode: Bluetooth Smart Ready devices
  include both Bluetooth low energy and Classic Bluetooth
  ex. a smartphone or PC
fundamentally different technologies from an application perspective

## Slide 6: Protocol Basics

## Slide 7: Physical Layer
Contains analog communications circuitry
2.4 GHz ISM (Industrial, Scientific, and Medical) band
  divided into 40 channels (37 connection and 3 advertising channels)
Frequency hopping spread spectrum
  a concept for having wireless radio signals switch quickly among many different frequency channels
  minimizes the effect of any radio interference
  Hedy Lamarr
Gaussian Frequency Shift Keying (GFSK) modulation

## Slide 8: Link Layer
When not in an active connection
  Advertiser
    A device sending advertising packets
  Scanner
    A device scanning for advertising packets
When in a connection
  Master
    A device that initiates a connection and manages it later
  Slave
    A device that accepts a connection request and follows the master’s timing

## Slide 9: Host Controller Interface
Separates Host from Controller
Allows them to communicate across a serial interface
A set of commands and events for the host and the controller to interact with each other, along with a data packet format and a set of rules for flow control and other procedures

## Slide 10: Logical Link Control and Adaptation Protocol
Protocol multiplexer
  encapsulates multiple protocols from the upper layers into the standard BLE packet format (and vice versa)
Performs fragmentation and recombination
  breaks up into chunks large packets from the upper layers to fit the 27-byte maximum payload size of the BLE packets (on the transmit side, and the opposite on the reception side)

## Slide 11: Attribute Protocol
Simple client/server stateless protocol based on attributes, each of which is assigned
  a 16-bit attribute handle,
  a universally unique identifier (UUID),
  a set of permissions, and finally, of course,
  a value
Each device is a client, a server, or both, irrespective of whether it’s a master or slave
A client requests data from a server, a server sends data to clients

## Slide 12: Security Manager
Both a protocol and a series of security algorithms
  Generate and exchange security keys, which then allow secure communication over an encrypted link, to trust the identity of the remote device, and finally, to hide the public Bluetooth Address if required
Defines two roles:
  Initiator
    Always corresponds to the Link Layer master and therefore the GAP central
  Responder
    Always corresponds to the Link Layer slave and therefore the GAP peripheral

## Slide 13: Generic Access Profile (1/2)
Provides a framework that any BLE implementation must follow
Makes your device visible to the outside world, and determines how two devices can('t) interact with each other
Specifies four roles that a device can adopt to join a BLE network

## Slide 14: Generic Access Profile (2/2)
Broadcaster (Optimized for transmit-only applications)
  Periodically sends out advertising packets with data
Observer (Optimized for receive-only applications)
  Listens for data embedded in advertising packets from broadcasting peers
Central (corresponds to the Link Layer master)
  always the initiator of connections
  essentially allows devices onto the network
Peripheral (corresponds to the Link Layer slave)
  uses advertising packets to allow centrals to find it and, subsequently, to establish a connection with it

## Slide 15: Generic Attribute Profile
Key section of the BLE specification
  every single item of data relevant to applications and users must be formatted, packed, and sent according to its rules
Adds a hierarchy and data abstraction model on top of ATT
Defines how data is organized and exchanged between applications
Maintains the same client/server architecture as ATT, but the data is now encapsulated in services, which consist of one or more characteristics, which can include one or more descriptors

## Slide 16: GATT Heart Rate Service

## Slide 17: Q & A
Thank you!